## Slide 1
[1] ‘Deep reinforcement learning for home energy management system control - ScienceDirect’. Accessed:
Aug. 15, 2025. [Online]. Available: https://www.sciencedirect.com/science/article/pii/S2666546820300434?via%3Dihub
Problem Addressed
High residential energy use (heating & hot water).
Need to optimize PV self-consumption by coordinating loads and solar production.
Method Used
Deep Reinforcement Learning (DRL)
Inputs: outdoor temp, indoor temp, DHW temp, PV production, time.
Actions: Heat ON, DHW ON, System OFF.
Neural net: 2 hidden layers, 16 neurons each.
Key Findings
8% average savings, up to 16% in summer.
Comfort maintained (<1% out of setpoints).
+9.5% PV usage and ~10% load shifting.
Limitations
Dependent on PV availability (weaker in winter).
Single case study; limited generalization.
Relevance to My Work
Similar RL can be used to find setpoints.
Neural net design (5 inputs, 3 outputs, 2 hidden layers) → challenge: choosing neurons & layers.
Find the accuracy of the current model(set point optimization) to compare with the various implementation of reinforcement learning

## Slide 2
[1]Q. Meng, S. Hussain, F. Luo, Z. Wang, and X. Jin, ‘An Online Reinforcement Learning-Based Energy Management Strategy for Microgrids
With Centralized Control’, IEEE Transactions on Industry Applications, vol. 61, no. 1, pp. 1501–1510,
Jan. 2025, doi: 10.1109/TIA.2024.3430264.
Problem
Uncertainty & intermittency of wind/solar in microgrids
Traditional methods lack real-time adaptability
Method
Online RL (SARSA) for joint scheduling of wind, solar & storage
Test case: residential microgrid with EV loads
Findings
Lower storage costs
Faster convergence than DQN
Limitations
Case-specific (residential EV microgrid)
Relevance
SARSA useful for fast, efficient RL in my work

## Slide 3
[1] H. Ganesh and B. Xu, ‘A review of reinforcement learning based energy management systems for electrified powertrains:
Progress, challenge, and potential solution’, Renewable and Sustainable Energy Reviews, vol. 154, p. 111833, Feb. 2022,
doi: 10.1016/j.rser.2021.111833.
The review paper (Ganesh & Xu, 2022) first introduces reinforcement learning theory before moving to applications.
It covers core concepts such as Markov decision processes, Bellman equations, value functions, and policies.
It classifies key algorithm families (tabular Q-learning, DQN, DDPG, actor–critic, safe RL, etc.) and their trade-offs.
The structure of the paper shows that theoretical grounding is essential before designing or applying RL methods.
Therefore, as a preliminary step in my thesis, I need to study the theory of reinforcement learning to understand algorithm selection, assumptions, and limitations.